## Slide 1: Overview of IEEE 802.1Qat [Stream Reservation Protocol]
By,
Mythili .R

## Slide 2: STREAM RESERVATION PROTOCOL [SRP]
Dynamic Control Protocol used to create path through a network for rank- based, latency guaranteed bandwidth reservations
Both talker & listener will reserve the bandwidth which is required for particular streaming in the concerned port and the talker will start streaming.
Verified by explicitly reserving the maximum bandwidth and so the port will not allow for new registrations
© Jasmin-Infotech Private Limited
2

## Slide 3: Terminology
Talker: Source of a stream
Listener: Destination of a stream
Domain: A connected set of talkers, listeners and bridges that support the same priority for an SR class.
Reservation: A network path between a talker and its listeners that supports the requested QOS.
© Jasmin-Infotech Private Limited
3

## Slide 4: Signaling Protocols
SRP utilizes three signaling Protocol:-
1.MMRP [Multiple MAC Registration Protocol](optional)
2.MVRP [Multiple VLAN Registration Protocol]
3.MSRP [Multiple Stream Registration Protocol]

## Slide 5: Signaling Protocols contd..
1.MMRP [Multiple MAC Registration Protocol]
  used to control the propagation of talker registrations throughout the bridged network
2.MVRP [Multiple VLAN Registration Protocol]
  used by end stations & bridges declare membership in a VLAN. This allow the data frame priority to be propagated along the path in tagged frames
  does not allow streams to be established across Bridge Ports that are members of the untagged set

## Slide 6: Signaling Protocols contd…
3.MSRP [Multiple Stream Registration Protocol]
  provides end stations with the ability to reserve network resources that will guarantee the transmission and reception.
  provides limited error reporting capability
  supports the concepts of data stream importance
EX: An emergency announcement would be flagged with a more important “rank” than a stream providing background music

## Slide 7: ARCHITECTURE OF MSRP
MRP application:
  provides stream resource registration service
MRP Attribute Declaration(MAD) function:
  provides common state machine Description defined for use in MRP based applications.
MRP Attribute Propagation(MAP) Function:
  provides Attribute propagation mechanism (in a case of two -port bridge)
MSRP—establishing SRP Domain Boundary for a particular SR class
  same SRP Domain –all systems having same priority for SR class
  SRP Domain Boundary –Different priority for the SR class
IEEE Std 802.1Qat-2010

## Slide 8: DMN [Designated MSRP Node]:
  provides the MSRP services for the shared medium
  determines each station’s ability to receive the MSRPDUs transmitted by other stations on the medium
  Control the reservations which are successful or not
IEEE Std 802.1Qat-2010
DMN
Non DMN port
DMN port
DMN port
Non DMN port
Non DMN port
Non DMN port
Ignore
MSRPDU
Process MSRPDU
TX
RX

## Slide 9: Qat Declarations
Declaration Meaning
TalkerAdvertise I have a stream if you want it
TalkerFailed I have a stream, but you can’t get it
ListenerReady I (we) want the stream and have network
resource available to receive it
Listener ready failed We want the stream and some can receive it and
some can NOT
Listener asking failed I (we) want the stream, but do NOT have
network resources to receive it
Network,IEEE Plenary Meeting – Mar 09 Vancouver, BC

## Slide 10: Talker and listener declaration contd…
IEEE Std 802.1Qat-2010
talker
listener
AVB Bridge 1
AVB Bridge 2
Talker advertise
Talker failed
Talker failed
Listener asking failed
Listener asking failed
Listener asking failed
Not sufficient BW
talker
listener
AVB Bridge 1
AVB Bridge 2
Talker advertise
Talker advertise
Talker advertise
Listener ready
Listener ready
Listener ready
Sufficient bandwidth
Fig: Talker and listener declaration in the case of two-port bridge

## Slide 11: Talker and listener declaration contd…
Network,IEEE Plenary Meeting – Mar 09 Vancouver, BC
talker
listener
Talker advertise
Listener ready failed
Not sufficient BW
talker
listener
Talker advertise
Listener ready
Sufficient bandwidth
Fig: Talker and listener declaration in the case of end station
listener

## Slide 12: Behavior of Bridges
MSRP aware bridges register and de-register talker and listener declarations on the bridge ports.
Changes in the state of registrations are processed by MSRP attribute propagation function and disseminated in the network by making or withdrawing talker and listener declarations.
Talker declarations to all other bridge ports
TalkerPruning: limit the Talker declarations to ports that have the streams destination_address in the MMRP MAC Address Registration Entries.
Listener declaration to the Bridge Port with the associated Talker declaration (matching streamID)
Blocked Declaration - Declaration is said to be blocked if the Spanning Tree instance identified on that bridge port has any value other than forwarding.
IEEE Std 802.1Qat-2010

## Slide 13: Definition of MSRP application
1. Definition of internal state variables
a) Port Media Type
b) Direction(‘0’for talker attributes, ‘1’ for listener attributes)
c) Declaration Type
d) SRP parameters
2. Definition of MRP protocol elements
a) MSRP application address
b) MSRP application EtherType
c) MSRP Protocol Version
d) MSRP Attribute Type definitions
e) MSRP Attribute Length definitions
f) MSRP Attribute List Length definitions
g) MSRP Vector definitions
h) MSRP FirstValue definitions (Stream reservations)
i) MSRP FirstValue definitions (Domain discovery)
IEEE Std 802.1Qat-2010

## Slide 14: Definition of MSRP application contd…
a)Port media type
i)Access Control Port:
Transmitter controls access to the medium on which it is sending, so it is either the
DMN for a shared medium, or it is a port on a full-duplex point-to-point medium
ii) Non-DMN shared medium Port:
Transmitter is attached to a shared medium, but does not control access to
the medium.
b) Direction
‘0’for talker attributes, ‘1’ for listener attributes
c) Declaration Type
For a Talker, 1.advertise
2.failed
For a listener, 3.ready
4.Ready failed
5.Asking failed
IEEE Std 802.1Qat-2010

## Slide 15: SRP Parameters
a) Port Tc Max Latency: The maximum per-port per-traffic class latency(in ns),a frame may experience through the underlying MAC service
b) talkerPruning: limit the Talker declarations to ports that have the streams destination_address in the MMRP MAC Address Registration Entries.
c) streamAge: A per-port per-stream 32-bit unsigned value used to represent the time(secs) .This value is used when determining which streams have been configured the longest.
d) msrpEnabledStatus: When MSRP is enabled on a device it shall cause a reset of all MSRP state machines on all ports.
e) msrpPortEnabledStatus: When MSRP is enabled or disabled on a port of a device it shall cause MAP to be rerun on all MSRP enabled ports so existing attributes can be propagated to the port just enabled
IEEE Std 802.1Qat-2010

## Slide 16: SRP Parameters contd…
f) msrpMaxFanInPorts: The total number of ports on a Bridge that are allowed to establish reservations for inbound Streams.
g) msrpLatencyMaxFrameSize: Calculation of the maximum latency through a bridge is in-part related to the maximum size of an interfering frame
h) SRPdomainBoundaryPort: A per-port, per-SR class, Boolean parameter that contains the value TRUE if the port is an SRP Domain Boundary Port otherwise it contains the value FALSE
i) SR_PVID: The Stream Reservation Port VLAN Identifier (SR_PVID) is a per-port parameter that contains the default VLAN ID for Stream-related traffic.
IEEE Std 802.1Qat-2010

## Slide 17: SRP Parameters contd…
2. Definition of MRP protocol elements
a)MSRP application address
The group MAC address used as the destination address for MRPDUs destined for MSRP Participants shall be the group MAC address for Individual LAN Scope group address, Nearest Bridge group address.
b)MSRP application EtherType
c)MSRP protocol version
defined by the hexadecimal value 0x00
IEEE Std 802.1Qat-2010
Assignment | Value
MMRP EtherType | 88-F6
MVRP EtherType | 88-F5
MSRP EtherType | 22-EA

## Slide 18: SRP Parameters contd….
d)MSRP AttributeType definitions
Talker Advertise Vector Attribute Type:
to identify a sequence of values of Talker advertisements for related Streams that have not been constrained by insufficient bandwidth or resources.
Talker Failed Vector Attribute Type:
to identify a sequence of values of Talker advertisements for related streams that have been constrained by insufficient bandwidth or resources.
Listener Vector Attribute Type:
to identify a sequence of values of Listener requests for related streams regardless of bandwidth constraints.
Domain Vector Attribute Type:
to identify a sequence of values that describe the characteristics of an SR class.

## Slide 19: contd…
Attribute type values
IEEE Std 802.1Qat-2010
Attribute type | value
Talker advertise vector | 1
Talker failed vector | 2
Listener vector | 3
Domain vector | 4
d)MSRP Attribute Length definitions
Attribute type | Value
Talker advertise vector | 25 (0x19)
Talker failed vector | 34 (0x22)
Listener vector | 8
Domain vector | 4

## Slide 20: SRP Parameters contd….
f)MSRP Attribute List Length definitions
an unsigned binary number equal to the number of octets contained within the Attribute List
used when calculating the number of octets to skip to proceed the next message or message end mark in MRPDU.
g)MSRP Vector definitions
1.MSRP Three Packed Events
Three Packed Events BYTE ::= (((((first Attribute Event) *6) + second Attribute Event)*6) + third Attribute Event)
2.MSRP Four Packed Events
Only used by listener vector attribute type
a)Ignore c)ready failed
b)ready d)asking failed
IEEE Std 802.1Qat-2010

## Slide 21: SRP Parameters contd…
h) MSRP First Value definitions (Stream reservations):
Four Attribute Declarations defined for MSRP :
Talker Advertise
Talker Failed
Listener attributes
The fourth attribute type, Domain, is used to discover the SRP domain
IEEE Std 802.1Qat-2010

## Slide 22: SRP Parameters contd...
MSRP First Value (Domain discovery):
The First Value for Talker Advertise, Talker Failed, and Listener attributes in MSRPDUs exchanged according to the protocol.
a) The first eight octets contain the StreamID
b) Following the StreamID are eight octets containing the DataFrameParameters
c) Following the DataFrameParameters are four octets containing the Tspec
d) Following the TSpec is one octet containing the PriorityAndRank
e) Following the PriorityAndRank are four octets containing the Accumulated Latency
f) Following the AccumulatedLatency are nine octets containing the FailureInformation
IEEE Std 802.1Qat-2010

## Slide 23: REFERENCE:
IEEE Std 802.1Qat-2010 sponsored by LAN/MAN committee, IEEE computer society
Designated MSRP Node handling on 802.11 Network,IEEE Plenary Meeting – Mar 09 Vancouver, BC
IEEE Std 802.1Qat-2010